## Slide 1
Enhancing Early Diagnosis of Autism with Machine Learning Algorithms Using Postural Control Features
There exists many tests both behavioral and physical to diagnose autism in an individual. However, there is no absolute medical test for diagnosis. By using the data from a child's postural sway, we can use machine learning to devise a method of accurately predicting and classifying autism at an early age.
Hayden Cressman
Mentor: Yumeng Li, Ph.D.
Abstract
Autism spectrum disorder is known to cause deficits in motor functionality and stability when compared to children of typical development. The cause of this is still under research, but it is quantifiable and usable for classification.
References:
https://www.ncbi.nlm.nih.gov/pmc/articles/PMC4267489/
https://www.autismspeaks.org/autism-statistics-asd
https://www.ncbi.nlm.nih.gov/pmc/articles/PMC5674672/
Purpose
In total there were 40 unique TD subject trials and 24 ASD subject trials. For this test we used a force plate and ran each test for 30 seconds at a sampling rate of 60 hz. This gives us their center of pressure data from which we can determine several things such as:
Displacement in the Mediolateral and Anteroposterior Directions
Area of Postural Sway
Multiscale Entropy in the Mediolateral and Anteroposterior Directions
Complexity Index based off the Multiscale Entropy
Methods
The precision of each classification model can be seen below. Since we are working with a small sample size with possibility of outliers, the precision is fairly high all around. The data was run using a 70-30 split on the total data set.
Findings
Chart: Classification Model Precisions
| Knearest | Logistic Regression | Decision Tree | Compliment Naïve Bayes
 | 0.85 | 0.9 | 0.9 | 0.75
Mediolateral Multiscale Sample Entropy
Anteroposterior Multiscale Sample Entropy
 | 0.0 | 1.0 | accuracy | macro avg | weighted avg
K-Nearest |  |  |  |  | 
precision | 0.9167 | 0.17500 | 0.85 | 0.8333 | 0.86
recall | 0.8462 | 0.8571 | 0.85 | 0.8516 | 0.85
f1-score | 0.8800 | 0.8000 | 0.85 | 0.8400 | 0.85
support | 13.00 | 7.00 | 0.85 | 20.00 | 20.00
Logistic Regression |  |  |  |  | 
precision | 1.0000 | 0.7778 | 0.90 | 0.8889 | 0.92
recall | 0.8462 | 1.0000 | 0.90 | 0.9231 | 0.90
f1-score | 0.9167 | 0.8750 | 0.90 | 0.8958 | 0.90
support | 13.00 | 7.00 | 0.90 | 20.00 | 20.00
Decision Tree |  |  |  |  | 
precision | 0.9231 | 0.8571 | 0.90 | 0.8901 | 0.90
recall | 0.9231 | 0.8571 | 0.90 | 0.8901 | 0.90
f1-score | 0.9231 | 0.8571 | 0.90 | 0.8901 | 0.90
support | 13.00 | 7.00 | 0.90 | 20.00 | 20.00
Compliment Naïve Bayes |  |  |  |  | 
precision | 0.8333 | 0.6250 | 0.75 | 0.7292 | 0.76
recall | 0.7692 | 0.7143 | 0.75 | 0.7418 | 0.75
f1-score | 0.8000 | 0.6667 | 0.75 | 0.7333 | 0.75
support | 13.00 | 7.00 | 0.75 | 20.00 | 20.00
Eyes Open
Eyes Closed